## Slide 1: Instability processing
Space for further information
Institute · Department · Title / first / last name · email · www.hzdr.de

## Slide 2: Goal and Strategy
Afinger
Atotal
Raw image
Segmentation
(region growing)
Intensity filter
(intensity window)
Dilation/Erosion
Instability segmentation

## Slide 3: Input data
Different gap heights
0.1 mm
0.5 mm
0.6 mm

## Slide 4: results
Intensity window method (area ratio calculation)
Ratio over time can be investigated but comparing between cases is of most interest (all_cases.csv)

## Slide 5: results
Region growing
Contour evolution over time can be plotted

## Slide 6: Conlusion
Initial processing of nearly all provided cases done
      instability area
      instability boundary
      Area ratio
  Developed methods can be applied to further experiments as long as data is provided in the same way
  Methods can be changed/ further improved
      Using background substracted data as input for region growing (might improve instability finger detection)
      Dynamically chosing intensity window boundaries based on image features
      Software could be adopted to recently introduced FWDT gitlab group standards
  All results are here: \\gssnas\bigdata\FWDT\DFischer\image_proc
  The source code is here: https://github.com/fischer-sw/instability-processing

## Slide 7: Methodology region growing
Base image
Find camera by darcest pixel in specific region
Segement camera with found seed (limit threshold if 4e4 pixels are detected)

## Slide 8: Methodology region growing
Set instability seeds based camera segmentation (determine main axis with bounding box  cabel detection)
Determine threshold by looking at growth rate of segmented area (if rate > 2 move 4 steps back)

## Slide 9: Methodology region growing
Clean instability segmentation by Dilation and Erosion + only keep area with longest contour
Close hole in instability by using main axis (search points most left above and bellow the yellow point)
- if the hole is not closed just fill
the camera segmentation
Hole closing successful
Hole closing not successful

## Slide 10: Methodology region growing
Fill closed instability
Generate contour from instability